## Slide 1
01
DC Electrical
Machines
Motors • Generators • Commutation • Real-world examples
training slide deck
20 slides
N
S
split ring
Electrical energy ⇄ mechanical rotation

## Slide 2
02
Learning route
From simple motor action to dynamos in everyday use
1
Construction
2
Motor action
3
Brushes & split rings
4
Fleming rules
5
Stator / rotor
6
Field systems
7
Starting
8
Starter motor
9
DC generator
10
Bicycle dynamo
By the end, learners should be able to explain how a DC machine converts energy, identify key parts, and describe common starting and application issues.
DC Electrical Machines

## Slide 3
03
What is a DC electrical machine?
The same core machine can be used as a motor or as a generator
MOTOR
→ electrical in
N
S
split ring
→ rotation out
GENERATOR / DYNAMO
→ rotation in
N
S
split ring
→ electrical out
• Current, magnetic field and force are linked.
• Mechanical rotation and induced voltage are linked.
• The commutator controls the external DC connection.
DC Electrical Machines

## Slide 4
04
Simple DC motor construction
The minimum parts needed to produce rotation
N
S
armature coil
shaft
carbon
brushes
split-ring
commutator
• Stator: fixed magnetic field
• Rotor/armature: rotating coil
• Commutator: reverses coil connections
• Brushes: sliding electrical contact
DC Electrical Machines

## Slide 5
05
Simple DC motor operation
A current-carrying conductor in a magnetic field experiences a force
N
S
current
out of page
⊙
⊗
opposite forces create torque
• Force direction depends on field and current direction.
• Opposite sides of the coil are pushed in opposite directions.
• The pair of forces creates a turning moment.
Key idea: motor action converts electrical energy into mechanical movement.
DC Electrical Machines

## Slide 6
06
Split rings and carbon brushes
How a DC motor keeps turning in the same direction
carbon brush
segment A
segment B
carbon brush
insulated gap
• Split ring = two insulated copper segments.
• Brushes stay fixed while the commutator rotates.
• Every half turn the coil connections swap.
• This reverses coil current at the right time.
Result: torque stays in the same rotational direction.
DC Electrical Machines

## Slide 7
07
Fleming’s left-hand rule
Used for motors: field + current gives force / motion
Motion / Force
Field N→S
Current + to −
Left hand = motor
• Thumb → Motion / force on conductor
• First finger → magnetic Field direction
• Second finger → conventional Current direction
Quick use: set two known directions, then the third points to the missing direction.
DC Electrical Machines

## Slide 8
08
Stators and rotors
Two key mechanical groups in a rotating electrical machine
STATOR: fixed part
ROTOR / ARMATURE: rotating part
• Stator provides the magnetic field.
• Rotor carries conductors and turns on bearings.
• Air gap must be small and uniform.
• Commutator sits on the rotor shaft in many DC machines.
DC Electrical Machines

## Slide 9
09
Permanent-magnet DC machines
The stator field is provided by permanent magnets
N
S
split ring
fixed field
compact
efficient at small sizes
• No field winding or field supply needed.
• Simple control by changing armature voltage or using PWM.
• Common in small fans, toys, actuators, pumps and automotive auxiliaries.
• Field strength is not easily adjustable.
Typical observation: reversing the supply reverses motor direction.
DC Electrical Machines

## Slide 10
10
Electromagnet field DC machines
The stator field is produced by coils wound on pole pieces
N
S
field coils
• Field current controls magnetic flux.
• Can be connected separately, in series or in shunt with the armature.
• Series field gives high starting torque, useful for starter motors.
• Extra copper and losses compared with permanent magnets.
Design trade-off: controllability versus complexity, heat and cost.
DC Electrical Machines

## Slide 11
11
Commutation and continuous rotation
The commutator flips coil current every half turn
N
S
1
Torque starts turn
N
S
2
Connections swap
N
S
3
Torque continues
Without commutation, the torque would reverse every half-turn and the rotor would not maintain useful rotation.
DC Electrical Machines

## Slide 12
12
Starting issues in DC motors
At standstill, there is no back EMF to limit armature current
V = Eᵦ + IₐRₐ
At start: Eᵦ ≈ 0
Armature current
start
running
light load
• Very low armature resistance can cause large inrush current.
• High current can damage brushes, commutator and windings.
• High torque can shock-load the mechanical system.
DC Electrical Machines

## Slide 13
13
Managing motor starting
Limit current until speed and back EMF build up
Series resistor
Temporary resistance reduces inrush current.
Electronic drive
PWM or controlled ramp increases voltage gradually.
Protection
Fuse, overload and thermal protection sized for the application.
Interlocks
Prevent starting under unsafe mechanical conditions.
Education safety note: use low-voltage supplies, current limiting, guarded rotating parts and clear stop controls.
DC Electrical Machines

## Slide 14
14
Example: car starting motor
A compact high-current DC motor used for a short duty cycle
series-wound
DC motor
pinion
flywheel ring gear
solenoid engages gear and switches high current
• Very high starting torque.
• Operates for a few seconds only.
• Large current from the battery.
• Typically uses a solenoid, pinion and reduction gearing.
DC Electrical Machines

## Slide 15
15
Car starter sequence
From key/button input to engine cranking
1
Driver start command
2
Solenoid pulls in
3
Pinion engages ring gear
4
High-current contacts close
5
Motor cranks engine
6
Engine fires; pinion disengages
Important design point: the motor is not designed for continuous operation; overheating occurs if cranking is prolonged.
DC Electrical Machines

## Slide 16
16
DC generators or dynamos
Mechanical rotation can generate a DC output
N
S
rotating coil
rotate
+
−
• Conductors cut magnetic flux when the rotor turns.
• An EMF is induced in the conductors.
• The commutator rectifies the coil output to give pulsating DC at the brushes.
Generator action converts mechanical input into electrical output.
DC Electrical Machines

## Slide 17
17
Fleming’s right-hand rule
Used for generators: field + motion gives induced current
Motion
Field N→S
Induced current
Right hand = generator
• Thumb → conductor Motion
• First finger → magnetic Field direction
• Second finger → induced Current direction
Memory aid: left = motors, right = generators.
DC Electrical Machines

## Slide 18
18
Dynamo construction and output
A commutator gives a unidirectional output at the brushes
N
S
split ring
mechanical input
DC output
pulsating DC after commutation
• Commutator reverses the internal coil connection each half-turn.
• External polarity stays the same at the brushes.
• Output ripple reduces with more coils and more commutator segments.
DC Electrical Machines

## Slide 19
19
Example: bicycle dynamo
Wheel motion drives a small generator for lighting
roller
dynamo
lamp / LED
load
• Tyre or hub rotation spins a magnet near a coil.
• Voltage rises with wheel speed.
• Modern systems often rectify and regulate the output for LEDs.
• Drag increases slightly when electrical load is connected.
DC Electrical Machines

## Slide 20
20
Recap: DC machines
Key checks for learners
1
Name the stator and rotor parts in a simple DC motor.
2
Explain why a split-ring commutator is needed.
3
Use Fleming’s left-hand rule to predict force direction.
4
Explain why a DC motor draws high current at start.
5
Describe how a bicycle dynamo generates electrical power.
Practical idea: run a low-voltage DC motor, observe starting current, reverse polarity, then spin the shaft and measure generated voltage.
End of deck