## Slide 1
01
Electromagnetism
Forces • magnetic circuits • induced voltage
F = B I l e = −N dΦ/dt E = B l v
N
S
motor effect

## Slide 2
02
The electromagnetism story
Three linked ideas appear again and again in machines, generators and transformers.
Current I
creates magnetic field
A coil or conductor produces flux Φ
Magnetic field B
pushes current
A current in a field experiences force F
Changing flux Φ
induces voltage e
A changing flux linkage creates EMF
Motor effect: F = B I l sinθ
Faraday: e = −N dΦ/dt
Motion EMF: E = B l v

## Slide 3
03
Force on a current-carrying conductor
A conductor carrying current at right angles to a magnetic field experiences a mechanical force.
N
S
B field: N → S
I out of slide
Force F
F = B × I × l
• B = magnetic flux density in tesla (T)
• I = current in amperes (A)
• l = active conductor length in metres (m)
• This form assumes the conductor is perpendicular to B

## Slide 4
04
Direction of force: Fleming’s left-hand rule
The three directions are mutually at right angles.
B
I
F
• First finger: field B (N to S)
• Second finger: conventional current I (+ to −)
• Thumb: force or motion F
• Reverse the current or field and the force reverses
Field × Current → Force

## Slide 5
05
Force calculation: worked example
Use consistent SI units before substituting into the equation.
F = B I l
Given
• B = 0.8 T
• I = 5 A
• l = 0.12 m
Substitute
F = 0.8 × 5 × 0.12
Answer
F = 0.48 N
active length l = 0.12 m
Tip: use only the conductor length inside the magnetic field.

## Slide 6
06
Force on a conductor at an angle
Only the component of conductor length perpendicular to the field contributes to force.
θ
B
I along conductor
F = B × I × l × sinθ
• θ is the angle between conductor and magnetic field
• At θ = 0°, sinθ = 0, so force is zero
• At θ = 90°, sinθ = 1, giving maximum force

## Slide 7
07
Angle dependence: sinθ
The magnetic force is proportional to the perpendicular component.
0°
30°
60°
90°
sinθ
θ
Fθ = Fmax × sinθ
Example when Fmax = 0.48 N
• 30°: 0.24 N
• 60°: 0.42 N
• 90°: 0.48 N

## Slide 8
08
Magnetic flux density B
Flux density describes how concentrated the magnetic flux is through an area.
higher B
lower B
B = Φ / A
• Φ = magnetic flux in webers (Wb)
• A = cross-sectional area in m²
• B = tesla (T) = Wb/m²
• A smaller area gives greater flux density for the same flux

## Slide 9
09
Magnetic flux density in an air gap
A near-uniform field lets us estimate force and induced EMF from B.
N
S
uniform gap
field
• B is stronger when flux is forced through a small gap
• B is weaker when flux leaks or spreads out
• In motors and generators, air-gap B is a key design value
• Education labs often use measured B from a gaussmeter / teslameter
Force and EMF calculations both need B

## Slide 10
10
Magnetic circuit: flux, MMF and reluctance
A magnetic circuit behaves like an electrical circuit analogy.
MMF
Fₘ = N I
magnetic “push”
Reluctance
R
opposes flux
Flux
Φ
magnetic flow
Core / gap
material + geometry
sets R
Φ = MMF / R

## Slide 11
11
Magnetic circuit – reluctance
Reluctance depends on path length, material permeability and area.
R = l / (μ₀ × μᵣ × A)
• l = magnetic path length (m)
• μ₀ = permeability of free space
• μᵣ = relative permeability of the material
• A = cross-sectional area (m²)
• Unit: ampere-turns per weber (A/Wb)
path length l
area A

## Slide 12
12
Reluctance and the air gap
Air has low permeability, so a small air gap can dominate total reluctance.
air gap
Rtotal = Rcore + Rgap
• Core: high μᵣ → low reluctance
• Air gap: μᵣ ≈ 1 → high reluctance
• Increasing the gap reduces flux for the same coil current
• Gaps are important in motors, solenoids and transformers

## Slide 13
13
Magnetic circuit – magnetising force
Magnetising force H is the MMF per unit magnetic path length.
H = N I / l
• N = number of turns
• I = coil current (A)
• l = magnetic path length (m)
• H is measured in A/m
• More turns or current gives a stronger magnetising field
N turns
current I
path length l

## Slide 14
14
From magnetising force to flux density
Permeability links H to B, but real iron saturates at high flux density.
B = μ₀ × μᵣ × H
• Permeability tells us how easily a material supports flux
• Higher μᵣ gives more B for the same H
• In saturation, extra current gives little extra flux
• Design avoids excessive current and overheating
B
H
saturation

## Slide 15
15
Induced voltage: Faraday’s law
A voltage is induced when flux linkage changes. The minus sign indicates Lenz’s law.
e = −N × dΦ/dt
• N = number of turns linked by the flux
• Φ = magnetic flux in webers (Wb)
• dΦ/dt = rate of change of flux
• Lenz’s law: induced current opposes the change causing it
N
S
changing Φ
induced e

## Slide 16
16
Generator EMF
A rotating coil changes its flux linkage, producing an alternating voltage.
• Coil rotates in a magnetic field
• Flux linkage varies sinusoidally
• EMF is greatest when the coil sides cut the field fastest
• Output frequency depends on rotational speed and pole count
e(t) is sinusoidal
N
S
AC output

## Slide 17
17
Generator EMF from straight-line motion
A conductor moving through a magnetic field cuts flux and generates a motional EMF.
E = B × l × v
• B = flux density (T)
• l = active conductor length (m)
• v = velocity at right angles to the field (m/s)
• Maximum when conductor, motion and field are mutually perpendicular
N
S
v
l
Example: 0.6 × 0.15 × 8 = 0.72 V

## Slide 18
18
Transformer induced voltage
A sinusoidal core flux induces voltage in each winding.
Emax = N × A × B × ω
ω = (2 × π × n) / 60
• N = turns on the winding
• A = core cross-sectional area (m²)
• B = peak flux density (T)
• ω = angular speed in rad/s
• n = rotational speed in rpm for the equivalent rotating field
primary
secondary

## Slide 19
19
Equation summary: choose the right model
Start from the physical situation, then select the matching equation.
Current in B field
F = B I l
use when conductor is at 90° to B
Conductor at angle
F = B I l sinθ
use θ between conductor and field
Flux density
B = Φ / A
flux spread over area
Reluctance
R = l/(μ₀ μᵣ A)
magnetic path geometry + material
Magnetising force
H = N I / l
coil MMF per metre
Faraday
e = −N dΦ/dt
changing flux linkage
Motion EMF
E = B l v
moving conductor cuts flux
Transformer peak
Emax = N A B ω
sinusoidal core flux

## Slide 20
20
Learning check and practical notes
Use the questions to test understanding before practical work.
• A conductor carries 3 A in a 0.5 T field over 80 mm. What force acts at 90°?
• What happens to force when the conductor angle is changed from 90° to 30°?
• Why does a small air gap greatly increase reluctance?
• A coil has twice the turns. What happens to induced voltage for the same flux change?
• For E = B l v, which three directions should be perpendicular?
Practical safety
• Keep currents within rated limits
• Avoid overheated coils
• Secure moving conductors
• Use SELV supplies for education work
Observe → measure → calculate → compare