## Slide 1
Electrical Machines
Shunt & Series Motors
DC Electrical Machines
Shunt motors • Series motors • Car starter motor circuit
Learning focus
Compare shunt and series field connections
Explain why starter motors use a series motor
Use typical starter voltage and current values
Recognise the starter solenoid circuit
M
TEACHING DECK • 10 SLIDES
Notes: A 10-slide lesson deck regenerated using the user supplied Matrix master file style.

## Slide 2
Electrical Machines
Field Connections
Two common wound-field DC motors
Both are brushed DC motors, but the stator field is connected differently.
Shunt motor: field winding is connected across the supply in parallel with the armature.
Series motor: field winding is connected in series with the armature, so the same current flows through both.
+
−
SHUNT FIELD
A
ARMATURE
parallel paths
+
−
SERIES FIELD
A
ARMATURE
Shunt: near constant field
Series: field strength rises with load current

## Slide 3
Electrical Machines
Shunt Motors
Shunt motor: stable speed under changing load
The field current is set mainly by the supply voltage and field resistance.
+
−
SHUNT FIELD
A
ARMATURE
parallel paths
Main points
Field winding: many turns, relatively high resistance
Armature current changes with mechanical load
Good speed regulation for many teaching examples
Do not run with field circuit open: speed can rise dangerously
COMMON USES
Fans, blowers, machine tools, test rigs and applications needing reasonably constant speed.

## Slide 4
Electrical Machines
Shunt Motor Behaviour
Shunt motor characteristics
Useful when steady speed is more important than very high starting torque.
Load torque
Speed
Small speed drop as load increases
Armature current
Torque
Torque rises approximately with armature current
For a shunt motor, the field is almost constant, so torque is mainly controlled by armature current.

## Slide 5
Electrical Machines
Series Motors
Series motor: high starting torque
The same current flows through field and armature, making the field strong at start-up.
+
−
SERIES FIELD
A
ARMATURE
Why torque is high at start
At standstill there is little back EMF
Large starting current flows
Field flux and armature current are both high
Result: very high starting torque
Important: a DC series motor should not be run unloaded because speed may rise excessively.

## Slide 6
Electrical Machines
Comparison
Shunt motor vs series motor
The field connection changes starting torque, speed regulation and safe operation.
Feature
Shunt motor
Series motor
Field connection
Parallel with armature
Series with armature
Starting torque
Moderate
Very high
Speed behaviour
Fairly constant
Varies strongly with load
No-load operation
Avoid field failure
Do not run unloaded
Good examples
Fans, test rigs, constant-speed drives
Starter motors, hoists, traction-style loads
Classroom shortcut: shunt = steady speed; series = strong start.

## Slide 7
Electrical Machines
Car Starter Motor
Car starter motor: a practical series motor
A starter motor needs a short burst of very high torque to crank the engine.
Pinion gear engages the flywheel, then the motor cranks the engine.
Why series?
Maximum torque is needed at zero speed
Low supply voltage means very high current
Operation is brief, so heating is managed by duty cycle
Solenoid both switches current and moves the pinion
SERIES MOTOR EXAMPLE

## Slide 8
Electrical Machines
Starter Current
Example starter motor voltage and current
Values vary with engine size, temperature, battery condition and motor design.
12 V
typical light-vehicle battery supply
150–300 A
example cranking current range
500 A+
possible cold-start or stall peak
Example calculation: P = V × I = 12 V × 250 A = 3000 W ≈ 3 kW
Teaching note: keep starter motor demonstrations controlled; high current can overheat cables and contacts quickly.

## Slide 9
Electrical Machines
Solenoid Circuit
Starter circuit with solenoid
The solenoid is both a relay and actuator: it closes the high-current contact and engages the pinion.
+
−
12 V battery
Ignition
START
SOLENOID COIL
Heavy solenoid
contacts
M
Series
starter motor
magnetic pull closes contacts
Low-current control path
High-current motor path
The small START switch does not carry starter current.

## Slide 10
Electrical Machines
Summary
Key takeaways
Use the motor connection to predict behaviour and choose the right application.
Shunt motor: field is parallel with armature, giving relatively steady speed.
Series motor: field and armature carry the same current, giving very high starting torque.
Car starter motor: series motor with a solenoid to switch high current and engage the pinion.
Typical example: 12 V system, about 150–300 A cranking and higher cold-start peaks.
Safety reminder: high-current DC systems need short duty cycles, secure connections, suitable cables and guarded rotating parts.
End of section